## Slide 1: ASR/KWS Test Automation
Lixun Xia
2018-04-17

## Slide 2: Module Test (Interface)
1. Play and recording by scripts (Matlab)
2. File IO: Matlab <-> DUT
3. File IO: Matlab <-> Scoring Server
4. Calibration

## Slide 3: Module Test (Interface)
1. Play and recording by scripts (Matlab) OK
2. File IO: Matlab <-> DUT OK
3. File IO: Matlab <-> Scoring Server OK
4. Calibration Working progress…

## Slide 4: 1. Play and recording by scripts (Matlab)
system()
In Matlab
Play-Record exe
PortAudio + ASIO

## Slide 5: 1. PortAudio + ASIO (For Windows Only)
Driver to FireFace sound cards via ASIO
Build with latest portaudio (v19) with ASIO SDK
MSVC 17 project file included
\Test-Automation-ASR-KWS\portaudio\build\msvc\
Output: portaudio_X64.dll
portaudio_X64.lib

## Slide 6: 1. Play-Record Application (.EXE)
Simple executable (Play, Record, Play and record)
Build on top of portaudio_X64.dll and portaudio_X64.lib
MSVC 17 project file included
\Test-Automation-ASR-KWS\standalone\
Output: PaDynamic.exe

## Slide 7: 1. System Call from Matlab
Matlab invokes play-record exe via system call
system(['PaDynamic.exe --play ess-stimulus.wav --record response.wav --rate 48000 --channels ', num2str(n_mic) ,' --bits 32'])
meaning: Play ess-stimulus.wav while do simultaneous recording synchronously to response.wav; sample rate 48000, record for n_mic channels, save recording as IEEE_FLOAT.
Code review [\Test-Automation-ASR-KWS\impulse_response_exponential_sine_sweep.m]

## Slide 8: 2. File IO: Matlab <-> DUT
Via SDB
File transfer via WIFI socket. (working progress…)
Since Jungle has made DUT control .bat scripts, we use them for matlab system call.
Code Review [\Test-Automation-ASR-KWS\file_io_dut_sdb.m]

## Slide 9: 3. File IO: matlab <-> Scoring server
Separate scoring machine: don’t load the measurement PC
File transfer via ssh
Put folder \Test-Automation-ASR-KWS\WakeupScoring_Tool_2.2\ to the home path of an Ubuntu 14.04 machine
Read \Test-Automation-ASR-KWS\WakeupScoring_Tool_2.2\README
Code Review [\Test-Automation-ASR-KWS\file_io_score.m]

## Slide 10: 3. File IO: matlab <-> Scoring server
On the server side:
Lux scoring tool input requires: mono, 16-bit, 16000 Hz.
Wrappers of the scoring tool: format conversion (ffmpeg)
resample/channel selection (sox)
control logic/report generation (julia)
ffmpeg/sox/julialang are just personal flavor.

## Slide 11: 4. Calibration
Mouth, SPL: fireface(play) -> fireface(record, ref mic @DUT)
Mouth, equalization: fireface(play) -> fireface(record, ref mic @MRP)
Noise, ind./all Spks: fireface(play) -> fireface(record, ref mic @dut)
Echo: DUT(play) -> fireface(record, ref mic @0.8m to DUT)
Ref mic level calibration: Calibrator -> fireface(record)

## Slide 12: 4. Other measurement tasks.
ERLE: DUT(play) -> DUT(record)
Mic distortion/impulse: fireface(play) -> DUT(record)
Turn-table: COM/USB to Matlab host
GREEN: Interface OK
BLUE: interface under construction…

## Slide 13: 5. Conclusion
Matlab seems to be a nice automation tool (dynamic, visualization)
Included a codebase for ASR/KWS automation to start with
Need to finish blue items ASAP.
Please correct my errors and suggest better methods, thank you!